## Slide 1: Quiz
Design a circuit which implements 4-bit incrementing/decrementing use a 4-bits full adder: when the input S=0, the circuit performs increment, when S=1, the circuit performs decrement.
Design a counter, when the control signal C=1, the counting sequence is 000100110111011000; when C=0, the counting sequence is 000100110010011000. Please write the state diagram, state table, next state function, output function and draw the circuit.