## Slide 1
10月25日随堂练习
3.8
2.16（a) 2.24(b)
2.19(c)
2.34

## Slide 2
11月日随堂练习

## Slide 3: Quiz2
Simplify the following with formulas and calculate the gate input cost for the original F and the simplified result. (6 pts)
For the following function, answer questions:
F(A, B, C, D) = ∑m(0,1,2,3,6,8) + ∑d (10,11,12,13,14,15)
  Draw the K-map and express F in product-of-maxterms algebraic form (∏M(…)); (4 pts)
  Circle the essential prime implicants and list the corresponding AND terms; (6 pts)
  Perform the optimization in the form of SOP and POS; (4 pts)

## Slide 4
一、填空题
三态缓冲器的输出有________个状态，若将几个三态缓冲器的输出端并联在一起，则最多允许__________个三态缓冲器输出使能。
数制转换：(17.5)8 = (______)10= (________)16。
(-7.7)10的8位机器数（3位小数，1位符号位）是_______；反码是_____________；补码是____________。
一个10位地址码、8位输出的ROM，其存储容量为_____________位。

## Slide 5
已知某函数
该函数的简形式的反函数
可以被用作可控门的逻辑门是_______________门。

## Slide 6
二. 选择题
二值逻辑处理二进制的变量，其变量只取____________个离散值。
A. 1个 B. 2个 C. 3个 D. 4个

## Slide 7
函数
的门输入成本G_________。
A. 9 B. 10 C. 11 D. 12
在四变量卡诺图中有___________个小格是“1”。
A. 13 B. 12 C. 6 D. 5

## Slide 8
 |  |  | Y |  | 
 | 1 |  | 1 | 1 | 
 |  |  | 1 |  | X
W |  | 1 | 1 |  | 
 | 1 | 1 | 1 | 1 | 
 |  | Z |  |  | 
下列卡诺图表示的函数中，质蕴涵项共有__________个。
A. 4 B. 5 C. 6 D. 7

## Slide 9
只读存储器 (ROM) 是由________与门陈列和_________或门陈列组成的组合逻辑结构。
可编程，固定的
B. 可编程，可编程
C. 固定的，可编程
D. 固定的，固定的

## Slide 10
（用公式化简，注明每步的主要公式）。
用卡诺图化简以下函数为最简与非-与非表达式：F = ∑m(0, 1, 5, 7, 8, 11, 13) + ∑d (3, 9, 12, 15)。（标出最大维块及对应的与项）

## Slide 11
分析下列逻辑电路，其中A、B、C、D为输入，F为输出。请列出F的真值表，写出F的逻辑表达式，分析此电路最大可能的功能。

## Slide 12
在下图的可编程逻辑阵列PLA上实现下列逻辑函数功能并作简要的设计说明（12分）：

## Slide 13
随堂练习3:
12月6日

## Slide 14
时序电路的次态不仅与当前输入有关，而且还与_______________有关。
通常情况下，主从触发器的建立时间要_____边沿触发器
电路输出方程只与电路现态相关的时序电路是_______________型电路。
如果对键盘上108个符号进行二进制编码，则至少要______位二进制数码。
传输延迟（Propagation Delay）是指变化的信号从_______________传输到____________所需要的时间，电路的处理速度与电路门的最大传输延迟成反比例关系。
用2个或非门构成的基本S-R锁存器两个输入同时为0时，其功能 为输出Q_____________________。

## Slide 15
基本R-S型触发器不具有___________功能。
保持 B. 翻转 C. 置1 D. 置0
存在“一次性采样”问题的触发器是________
A. S-R锁存器 B. D锁存器
C. 边沿触发的D触发器 D. S-R主从触发器

## Slide 16
设下图时序电路中门与触发器的参数如下：异或门的延时tpd=3.0ns，与门的延时tpd=1.5ns，触发器延时tpd=3.0ns，建立时间ts=1.0ns，保持时间th=0.25ns。外部输入需要在时钟脉冲上升沿的___________之前就需要确定下来。
A. 8.5ns B. 7.5ns
C. 6.5ns D. 5.5ns
A. 8.5ns B. 7.5ns
C. 6.5ns D. 5.5ns

## Slide 17
根据下图写出电路的输出方程、次态方程，
列出状态表，画出状态图。

## Slide 18
采用米利模型设计一个电路，来识别两个序列101和110。当识别到序列101时，电路输出10，当识别到序列110时，输出11。否则，电路输出00。请画出状态图、状态表、次态方程和输出方程，并画出电路图。

## Slide 19
随堂练习4
12月20日 (题中所有公式及图都需要化简，必须去掉等价状态）

## Slide 20: 填空
1 Given two 8-bit registers R1 and R2, with R1 = (1011 0101)2
and R2 = (0111 0110)2. After two microoperations:
R1  sr R1 and b) R1  R1⊕R2,
R1= (_ _)2.
Using a 4-bit synchronous binary counter to design a Module-8 counter, the activation of Load signal can be _____B_____.
A. Q2Q1Q0 B. Q2Q1Q0
C. Q2 Q1 Q0 D. Q2+Q1+Q0
2 74LS153 is a dual 4-to-1-line multiplexer, if the data input lines I0 ~ I3 = 1010, selection inputs S1S0 = 10, then the output of the multiplexer is Y=__________, if the output Y is required to be square wave, then the selection inputs S1S0 could be_______________.

## Slide 21
3 (2%) How many flip flops will be complemented in a 8-bit binary up counter to reach the next count after the count 10100011: _________.
4 What is the output function implemented by the following circuit： .

## Slide 22: 选择
1 Using a 4-bit synchronous binary counter to design a Module-8
counter, the activation of Load signal can be ________.
A. Q2Q1Q0 （上划线） B. Q2Q1Q0
C. ~Q2 ~Q1 ~Q0 D. Q2+Q1+Q0
2 Q3Q2Q1Q0 are the outputs of a synchronous BCD counter，Q3 is the most significant bit，then the output period of Q3 and its width of the positive pulse (HIGH voltage value) are_________.
10 clock periods, its width of the positive pulse is 1 clock period
10 clock periods, its width of the positive pulse is 2 clock period
16 clock periods, its width of the positive pulse is 2 clock periods
D. 16 clock periods, its width of the positive pulse is 10 clock periods

## Slide 23
3 Using synchronous binary counter to design a Module-N counter, the activation of Load signal is to make the counter_________ under the control of clock.
A. load the initial non-zero number at one time
B. initialize the starting states for all flip-flops at one time
C. load the initial number on the next clock transition before starting counting or when counting to N-1
D. none of the above
4 至少__________个4位二进制计数器可以构成N=2010的计数器。
A. 12 B. 11 C. 3 D. 2

## Slide 24
5 Given the Mod-N counter with synchronous reset signal shown below, N =
A 6 B 7 C 8 D 9

## Slide 25: Circuit design
A | B | X (A>B) | Y (A<B) | Z (A==B)
0 | 0 |  |  | 
0 | 1 |  |  | 
1 | 0 |  |  | 
1 | 1 |  |  | 
1 Magnitude comparators.
(1) Construct the Truth Table for a one-bit unsigned magnitude comparator. There are two inputs: A and B with three outputs: X, Y, Z, and X is Boolean value for logic A>B, Y for logic A<B and Z for logic A==B.

## Slide 26
2) Use “one 2-to-4 decoder” and some “logic gates” (i.e., OR, AND, and such) to implement this one-bit comparator.
(3) Take the 1-bit comparator you design as a building block (i.e., draw it as a box with 2 inputs and 3 outputs), now use two of these and other logic gates to design a 2-bit unsigned magnitude comparator. The new comparator consists of 4 inputs: A[1:0] and B[1:0], and 3 outputs: A>B, A<B, and A==B. Please show your logic circuits schematic and label the inputs and outputs properly.

## Slide 27: Sequential circuits design.
2 Design a 2-bit up/down saturating counter using D Flip-Flops and other basic gates: derive the state diagram, state table, and draw the circuits. The counter consists of 2 inputs (one for controlling direction, the other one is the clock) and 2 outputs that represent the current count value. The functionality of this counter is described in the pseudo code on the right.

## Slide 28
(1) Draw the State Diagram (Mealy or Moore)
(2) Derive the State Table, write down next state equations and output equations, and simplify them.